## Slide 1: Three Mile Island Site Transportation Infrastructure Evaluation
Northeast High-Level Radioactive Waste
Transportation Task Force Fall Meeting
Portland, ME
October 25-26, 2023
Miriam Juckett
Pacific Northwest National Laboratory

## Slide 2: Disclaimer
This is a technical presentation that does not take into account contractual limitations or obligations under the Standard Contract for Disposal of Spent Nuclear Fuel and/or High-Level Radioactive Waste (Standard Contract) (10 CFR Part 961).
To the extent discussions or recommendations in this presentation conflict with the provisions of the Standard Contract, the Standard Contract governs the obligations of the parties, and this presentation in no manner supersedes, overrides, or amends the Standard Contract.
This presentation reflects technical work which could support future decision making by the U.S. Department of Energy (DOE or Department). No inferences should be drawn from this presentation regarding future actions by DOE, which are limited both by the terms of the Standard Contract and Congressional appropriations for the Department to fulfill its obligations under the Nuclear Waste Policy Act including licensing and construction of a spent nuclear fuel repository.

## Slide 3: Locations of Commercial SNF
Commercial SNF R&D Facility
Naval Reactor Fuel (Idaho National Laboratory)
DOE Sites with SNF/HLW
Commercial HLW
Non-DOE Research Reactors
Commercial SNF Pool Storage (Away-From-Reactor)
Commercial SNF Dry Storage
Operating Commercial Reactor
“New Build” Reactor (Under Construction)
Shutdown Commercial Reactor
SNF – Spent Nuclear Fuel
Updated October 2022
Note: Symbols do not reflect precise locations
Locations of Commercial SNF
3
Western Sites Evaluated
Trojan
Humboldt Bay
Rancho Seco
San Onofre
Midwestern Sites Evaluated
Big Rock Point
Kewaunee
La Crosse
Zion
Fort Calhoun
Morris
(Operating)
Dresden
(Operating)
Palisades
Duane Arnold
Southern Site Evaluated
Crystal River
Eastern Sites Evaluated
Maine Yankee
Vermont Yankee
Yankee Rowe
Pilgrim
Connecticut Yankee
Oyster Creek
Indian Point
Three Mile Island

## Slide 4: Nuclear Power Plant Site Evaluations
The purpose of nuclear power plant (NPP) site evaluations is to:
  Confirm, gather, and identify gaps in information related to the inventory of spent nuclear fuel (SNF) and greater-than-Class C (GTCC) waste at the NPP sites
  Document conditions at the NPP sites at time of evaluation
  Evaluate site transportation experience and near-site transportation infrastructure at the NPP sites
Identify gaps in information needed to ship SNF and GTCC waste from the NPP sites
Based on the available information, identify options for transporting SNF and GTCC waste from the NPP sites

## Slide 5: NPP Site Evaluation Process
Extensive NPP site research
Planning with NPP Site
  List of questions submitted to NPP site about two months before site evaluation
  Coordinate regarding security access requirements and logistics
Planning with nearby railroads
  Federal Railroad Administration (FRA) leads this activity
  Identify potential transload locations
Planning with Federal, Tribal, State, and State Regional Group partners
  US Army Corps of Engineers and US Coast Guard if barging transport mode possible
  State Regional Groups will often assist in external engagement meetings
  Variety of State agencies will typically participate in a site evaluation
Planning with community engagement or advisory panels and local representatives
Logistics planning
These activities will typically take 6 months

## Slide 6: Sources of Information
Documents and Databases
  Technical reports, nuclear industry trade publications, newspapers, web
  Energy Information Administration (EIA) GC-859 Nuclear Fuel Data Survey Database
  Geographic Information System (GIS) databases
  Facility Interface Data Sheets (FIDS), Services Planning Documents (SPDs), Facility Interface Capability Assessment reports (FICAs), and Near-Site Transportation Infrastructure reports (NSTIs)
Independent Spent Fuel Storage Installation (ISFSI) Site Managers
  Confirmed information obtained from other sources
  Clarified current conditions at the sites
  Provided photos and other detailed information
Heavy Equipment Lifting, Rigging, and Transporting Companies
Google Earth
  Understand layout of sites
  Used to provide detailed maps of sites and ISFSIs
  Portray transload locations, and rail and heavy haul routes
Big Rock Point Reactor Pressure Vessel Heavy Haul
Photo courtesy of Barnhart Crane & Rigging
Maine Yankee Site

## Slide 7: NPP Site Inventories
NPP SNF site inventories based on the GC‑859 Nuclear Fuel Data Survey
  Database contains the characteristics of the fuel assemblies discharged from each reactor
  Most recent data through December 31, 2017
  Number of SNF assemblies, assembly ID and type, metric tons heavy metal (MTHM), discharge date, burnup, enrichment of SNF assemblies
Type and number of SNF storage systems (vendor and model) used at each site’s ISFSI
  Canisters containing SNF
  Canisters containing GTCC waste
  Loading maps, logs, etc.
Storage features/conditions
  Number of damaged fuel assemblies
  Number of high burnup fuel assemblies
  Canned/Not canned

## Slide 8: Site Conditions
On-Site Transportation Features
  On-Site Rail
  On-Site Roads for Heavy-Haul Trucks
  Barge Access
On-Site Equipment to Support Transportation Operations
  Transfer Casks
  Cranes and Rigging
On-Site Staging Areas for Transport Vehicles, Equipment and Operations Support
Photo courtesy
of Big Rock Point
Onsite Rail Spur at La Crosse
Big Rock Point Horizontal Transfer System
Photo courtesy
of La Crosse
Trojan Transfer Station
Photo courtesy of Trojan

## Slide 9: Near-Site Transportation Infrastructure and Experience
Evaluate transportation mode options for the NPP sites
National, Regional, or Short-Line Rail Access
  Condition and capacity of near-site commercial rail infrastructure
  Potential transload locations
  Site experience with rail shipments
Local Roads and Highways
  Distance to potential transload locations (rail spurs or sidings)
  Characteristics and condition of roads and associated infrastructure that would be used by heavy haul vehicles
  Site experience with heavy haul shipments
Barge Access
  Characteristics of onsite or nearby docks/slips/sidings/shorelines
  Site experience with barge shipments
Junction of Onsite Rail Spur and
Union Pacific Railroad at Zion
Current Condition of Connecticut Yankee Barge Slip
Low Overhead Bridge
Near Big Rock Point

## Slide 10: Transportation Mode Options
Notes: UPDATE GRAPHIC

## Slide 11: Key Parts of NPP Site Evaluations Are Site Visits
Twenty-two in-person NPP site evaluations conducted from August 2012 through September 2023
Site visits typically take place over three days
First day – NPP site
Second day – near-site transportation infrastructure
  Rail infrastructure
  Potential heavy haul truck routes
  Potential rail and barge transload locations
Third day – often spent meeting with community engagement or advisory panels and local officials

## Slide 12: Three Mile Island Site Visit

## Slide 13: Aerial View of Three Mile Island (TMI) Site
Photo of operating plant courtesy of
Located in the Londonderry Township of Dauphin County, Pennsylvania
Approximately 16 kilometers (10 miles) southeast of Harrisburg, PA and 4.8 kilometers (3 miles) south of Middletown, PA

## Slide 15
The plant takes its name from the oblong island in the Susquehanna River on which it is located.

## Slide 16: Three Mile Island Nuclear Station: Operations
Historic significance due to the partial meltdown of TMI Unit 2 on March 28, 1979 – the most significant nuclear accident in U.S. history.
TMI Unit 1
  Issued operating license in 1974
  Babcock and Wilcox Pressurized Water Reactor
  Continued operations until permanently shut down on September 20, 2019
  Owned by Constellation Energy Company
TMI Unit 2
  Issued operating license on February 8, 1978, commercial operations December 1978
  Babcock and Wilcox Pressurized Water Reactor
  Operated for only a few months before accident; never operated again
  Owned by TMI-2Solutions, an EnergySolutions subsidiary
Four TMI Cooling Towers - Looking North

## Slide 17: Three Mile Island Nuclear Station: Decommissioning
TMI Unit 1
  Original License Expiration: April 19, 2014
  Renewed License Expiration: April 19, 2034
  Permanent shutdown determination: April 2017
  All spent nuclear fuel (SNF) permanently removed from reactor: September 26, 2019
  All SNF placed in ISFSI: July 27, 2022
  SAFSTOR decommissioning status
TMI-1 cooling tower (left) Reactor Building (center)

## Slide 18: Three Mile Island Nuclear Station: Decommissioning
TMI Unit 2
  Damaged fuel and contaminated reactor vessel components removed from the site; placed into storage on the Idaho National Laboratory site.
  Removal actions completed by January 1990
  Very small amount of residual debris outside the reactor vessel remains to be removed
  Began SAFSTOR license status in 1993; recently transitioned to active decommissioning.
Evaluation focused on TMI Unit 1 (SNF on site)
Units collocated, so transportation infrastructure information considered for both Units
TMI-1 (left) and TMI-2 (right) Reactor Buildings

## Slide 19: Three Mile Island Nuclear Station: TMI-1 ISFSI
ISFSI construction March 2020 – July 2021
ISFSI loading campaign Oct 2021 – July 2022
46 NAC MAGNASTOR SNF storage systems
1665 SNF assemblies
1 NAC MAGNASTOR Greater Than Class C Waste (GTCC) canister
4 additional decommissioning GTCC canisters expected
MAGNASTOR Components
  Transportable Storage Container (TSC): Stainless steel cylindrical shell with welded lid; fuel basket structure
  Vertical concrete cask: holds and protects sealed TSC during ISFSI storage, provides radiation shielding, structural protection, and heat dissipation
Canisters can be shipped in MAGNATRAN transportation cask
TMI Cooling Towers and ISFSI
*Independent Spent Fuel Storage Installation = ISFSI

## Slide 21: TMI-1 ISFSI
Long View of ISFSI Pad
Cask Scale

## Slide 22: TMI-1 ISFSI
Layout of ISFSI with Cooling Tower
Corner View of ISFSI Pad

## Slide 23: Three Mile Island Nuclear Station: TMI-2 GTCC
Most fuel and debris already removed from site
Decommissioning estimated to produce additional 14-15 GTCC canisters
Plan to continue to use MAGNASTOR system
TMI-1 ISFSI pad expansion area; room for up to 27 casks
Looking South – Pad Expansion Space

## Slide 24: Vertical Cask Transporter
Disassembled Vertical Cask Transporter

## Slide 25: Site Rail Access

## Slide 28: Rail Line Area at North Entrance
Rail Line at North Bridge Entrance

## Slide 29: Rail Line Area at North Entrance
Chalked Rails with Weight

## Slide 30: TMI North Bridge
Built in 1960s to support rail and vehicle traffic
Steel superstructure with concrete composite deck and asphalt surface
Rail lines installed to support construction of both Unit 1 and 2 remain but have not been utilized since a 2014 transformer delivery
Rated currently for 40-ton weight limit; higher loads require evaluation
Repairs and upgrades planned for decommissioning

## Slide 31: TMI North Bridge
Site Entrance at North Bridge
Sign Postings at North Bridge

## Slide 32: TMI North Bridge
Heading West onto TMI Site
Rail Condition on Bridge

## Slide 33: Onsite Rail
Heading West onto TMI Site
Rail Condition at Entrance

## Slide 34: Onsite Rail
Rail Near Reactor Buildings
Rail Past North Bridge Entrance

## Slide 37: TMI South Entrance
Road Past South Bridge on Site Traveling North
South Bridge Entrance

## Slide 38: Rail Near TMI South Entrance
Norfolk Southern Rail Near South Bridge
Rail Bridge Near South Entrance

## Slide 39: Rail Near TMI South Entrance
Norfolk Southern Rail Near South Bridge

## Slide 40: Rail Yard Near TMI – Potential Interchange Point
Rail Yard at 3652 Industrial Road – Bridge Views

## Slide 41: Rockville Bridge – Rail Near TMI
Rockville Bridge Railroad Tracks (Norfolk Southern)

## Slide 42: Visited Several Potential Transload Locations
West of DuraBond Protective Coatings (2716 South Front Street, Steelton, PA)
Cleveland Cliffs Steel (215 S. Front Street, Steelton, PA)
Steelton Regional Water Treatment Plant (282 Christian St., Steelton, PA
Cleveland Cliffs Scrap Yard (near Christian St.)
Consolidated Scrap (1616 N. Cameron St. Harrisburg, PA)

## Slide 43: Planned Infrastructure Upgrade
    Cyan – Existing Rail Lines
    Blue – New Rail Spur
    Red – Excluded from Rail Scope
Courtesy of

## Slide 44: External Engagement
Extensive team participation
  Federal: DOE and National Laboratories, FRA, FBI, NRC
  State: PA Bureau of Radiation Protection, PA DOT, PA Emergency Management (PEMA) CSG-ERC
  Tribal: TRMTC
  Industry: Constellation, TMI-2 Solutions, Norfolk Southern
Meeting with TMI-2 Community Advisory Panel and local officials

## Slide 45: Site Summary
Transportable canisters
Abundant staging areas
Vertical cask transporter remains onsite
Direct rail access
No barge access
Heavy haul truck unlikely
Rail and bridge infrastructure improvements planned

## Slide 46: Status – Nuclear Power Plant Site Evaluations
All 22 decommissioned sites visited to date
Most recent site evaluations were of Morris (17) and Dresden (18) in May 2022, Indian Point (19) in July 2022, Palisades (20) in October 2022, and Three Mile Island in August 2023 (21).
Duane Arnold was final decommissioned site DOE visited (22): Sept. 2023

## Slide 47: Status – Nuclear Power Plant Site Evaluations
April 2021 update of the NPP site evaluation report posted on DOE-NE website (https://www.energy.gov/ne/articles/nuclear-power-plant-infrastructure-evaluations-removal-spent-nuclear-fuel)
  Includes 16 site evaluations through Oyster Creek (15) and Pilgrim (16)
Updated report 2023 to include up to Palisades
  Additional reports to come; may include volumes
Continue to collect data on conditions at previously visited sites
DOE intends to continue conducting site evaluations of additional NPP sites and to eventually conduct evaluations for all NPP sites

## Slide 48
Questions?